## Slide 1: BMS

## Slide 3: Battery Composition

## Slide 4: Battery

## Slide 5: Series and Parallel
Series :
Volatge Adds
Current: Constant
Parallel :
Volatge constant
Current adds

## Slide 6: BMS Architecture

## Slide 7: Charging and Discharging

## Slide 8: Working and Controls

## Slide 9: Charge rate
Battery Capacity : 100Ah - 1C rate
It can hold up to 5C
At 1C charge rate = 100A – 1hr
At 0.5C charge rate = 50A – 2hrs
At 5C charge rate = 500A – 20 mins

## Slide 10: LV and HV Operation
Low Voltage:
BMS is turned and monitoring the cell voltages butnot connected to battery through HV cables.
High Voltage:
BMS is turned on and the contactors are closed HV bus from battery is connected to load.

## Slide 11: Working of BMS

## Slide 12: Key Parameters
The BMS shall monitor and/or compute:
Battery-side Voltage (V_batt) – battery pack terminal voltage.
Bus-side Voltage (V_bus) – load/motor side voltage.
Pack Current (I_pack) – charging/discharging current.
Pack Temperature (T_pack) – battery temperature(s).
Contactor Feedback – status confirmation of precharge and main contactors.
SOC (State of Charge) – remaining battery capacity in %.
SOH (State of Health) – available capacity relative to new, in %.
Cycle Count – number of charge–discharge cycles completed.

## Slide 13
Battery
Load

## Slide 14: Operating States
OFF: Key switch OFF or system fault exit. All contactors open.
WAIT: Key switch ON, pre-checks, all contactors open.
PRECHARGE: Precharge sequence in progress. Precharge contactor closed until |V_batt – V_bus| ≤ 3V (within timeout).
HV: Main contactors closed, HV active on bus. Precharge contactor open.
FAULT: Any unsafe condition. Contactors opened immediately, logged.

## Slide 15: Precharge
Precharge protects power electronics from inrush current
Precharge resistor limits current when connecting battery to load/DC bus
BMS controls Precharge relay & main contactor
Sequence:
1.BMS checks voltage
2. Precharge relay closes – DC bus charges via resistor
3. When bus voltage ≈ pack voltage → Main contactor closes
4. Precharge relay opens
Fault → abort and open relays

## Slide 16: Contactor Control

## Slide 20: Battery Sizing

## Slide 22: SOH

## Slide 26: Contactor Monitoring Strategy

## Slide 27: Temperature Monitoring Strategy